The EvoStat
Evolution: on your schedule

This document describes the construction of an automated phagestat to maintain an evolving population of bacterial virus. The current device was designed to maintain a population of M13 phage using a supply of E. coli host cells but could be used for directed evolution of other organisms as it manages temperature, turbidity, reagent concentrations, and precise flow control.
Software for EvoStat

MAIN PROGRAM: INITIALIZE, RUN

INITIALIZE:
 Arduino discovery and initialization
Light testing (verify closed chamber)
Level detection, Prime Sequence if necessary

RUN
     for(i=0;i<normalcycles;i++)
if (temperature[t] < set_temp[t])
heater(t,ON);
else heater(t,OFF);
if (!check level) re-calibrate flow rate
if (turbidity > setpoint) open nutrient valve
if (bioluminescence) report activity

check temperature:
check nutrient temperature
   check host cell temperature
check lagoon temperatures

Arduino Command Reference

d – dump parameter values
s – save current values in EEPROM
r – restore parameter values from EEPROM
l1 – level detection (meniscus) lights on
l0 – level detection (meniscus) lights off
d
pN1 – pump N on
pN0 – pump N off
vN1 – valve N on
vN0 – valve N off
hN1 – heater N on (auto temperature control)
hN0 – heater N off (no temperature control)
Heaters 1-4=Lagoons, 5=Host Cells, 6=Nutrient Preheater
Pumps 1=Nutrient,2=Host Output,3=Inducer1,4=Inducer2,5=Waste
Valves 1=Nutrient,2=Host Output,3=Inducer1,4=Inducer2,5=Waste

Arduino Acquisition and Initialization
Logging

Calibrate Flow-Rate
V30,V40,V50 -Host Cells into lagoons, no lagoon outflow
monitor level increase rate and adjust timings 1-4
V30,V40,V20,V51 – Lagoon outflow only
monitor level decrease and adjust timings 13-16
        V31, V40, V20,V50 – Inducer1 inflow only
        monitor level increase and adjust timings 5-8
V30,V41,V20,V50 – Inducer 2 inflow only
monitor level increase and adjust timings 9-12

EvoStat part list with ordering information

Qnty	Description	URL	Price
10	3A rectifier diodes	Jameco diode	100 @ $10.00
2	71 RPM 12VDC gearhead motor	Jameco #155855	1 @ $21.95
16	Compression Valve Fitting (ABS)	3D Printer	-
1	Compression Valve Pointer (ABS)	3D Printer	-
16	3/32 Stainless Steel Welding Rod 4”		-
1	Chicago Metal 14” pizza crisper pan
5	12V DC Peristaltic pump
5	12V DC N/C valve
32	1K 1% metal film resistors	DigiKey resistors	5000 @ 42.75
2	10ft ¾” PVC pipe	Lowes / Home Depot
1	10ft 3” PVC pipe	“
4	¾ X ¾ X 1 PVC elbow	“
4	Sample valve fitting	3D Printer
4	¼-20 anodized speed nut
1	12” 4.75mm (.1875”) stainless steel rod	Online Metals	0.80
1	Surplus image scanner + stepper motor	Triangle E-cycling?	-
	RJ-45 inline couplers	Amazon	12 @ 12.00
	Ethernet cables w/ RJ-45 plugs
1	Ardweeny (auto sampler controller)	Solarbotics	9.95
1	Arduino Mega 2650 (main controller)	Amazon Mega 2650	14.99

	FOR WIRELESS LAGOONS:
4	Arduino Mini Pro (5V 16Mhz 368)	MinInTheBox	$3.95
4	Bluefruit EZ-link (Bluetooth FTDI)	AdaFruit	$22.50
4	HC-06 (alternative Bluetooth/slave only)	MiniInTheBox	$4.79
4	ULN2003	JameCo	0.35
1	7X9cm pre-drilled PC board 276-168	Radio Shack	$3.49
1	Connectors	MiniInTheBox	$1.99
1	Melexis 90614 PIR Temp sensor	DigiKey	$27.22

1	Heating wrap for Nutrient	Carboy Heater

1	Foscam 1.3M Wireless Outdoor Camera / alt/ Microsoft LifeCam VX-5000	Foscam	$259.99
8	Multi-color RJ-45 jacks	Amazon	4.99 each
8	Multi-color cables	Cable Matters	11.99
2	1 ¼” stainless steel hose clamp
100	½” #6 flat phillips sheet metal screws

Assemblies

1. Rotary Valve Assembly (1)
2. Priming pumps with valves (4)
3. Host Cell Stand – magnetic mixer + LED light + heater (1)
4. Lagoon Stands - magnetic mixer + LED light + heater (4)
5. Optical assembly (LED's, laser, PIR temperature sensor) (1)
6. Camera Mount
7. Stainless steel containment pan with leak sensors
8. Four-channel Auto sampler
9. Arduino Mega 2650 system controller

Connections

Four RJ-45 sockets on the main controller board connect to the four sub-systems.

Temp includes the main Host Cell container heating element (1 output) and the PIR temperature sensor (+5V, SCL, SDA, Gnd) and position feedback for Rotary Valve (Rotary In)

Flow connects to the first three priming pumps and valves (6 outputs Host, Inducer, Waste) and Rotary Valve motor (1 output plus 12VDC)

Mixers connects to the magnetic mixers for the host cell container and four lagoons (5 outputs), the host cell nutrient valve (1 output) and aeration (1 output), plus 12VDC mixer supply.

Lights connects to seven outputs: yellow meniscus lighting, white camera light, white, blue, green, and red backlight LEDs, laser, and 12VDC source.

Ethernet cable connections: Lights
Orange	+ 12V
Orange-white	Yellow LED
Green	Green LED
Green-white	White LED
Blue	Blue LED
Blue-white
Brown	Laser
Brown-white	Red

Ethernet cable connections: Mixers
Orange	+ 12V
Orange-white
Green	Host Cell container
Green-white
Blue	Lagoon 1
Blue-white	Lagoon 2
Brown	Lagoon 3
Brown-white	Lagoon 4

Ethernet cable connections: Flow (Pumps and Valves)
Orange	+ 12V
Orange-white	Rotary Valve Motor
Host Cell supply
Green	Pump 1
Green-white	Valve 1
Mutagenesis Inducer supply
Blue	Pump 2
Blue-white	Valve 2
Lagoon Outflow (waste)
Brown	Pump 3
Brown-white	Valve 3

Ethernet cable connections: Temperature Sensor/Heat control
Orange	+ 5V
Orange-white	SCL
Green	Ground
Green-white	SDA
Blue	Lagoon Heaters
Blue-white	Chamber Heat
Brown	Nutrient Heat
Brown-white	Host Cell heat

Length	type	diameter
1”	ring	2”
1”	split	2”
1”	split	1.5”
1”	2 spacers	1.5”
1.5”	Double split	3/4”

System Diagram

Cellstat
System Controller
Raspberry Pi

Phagestat
Lagoon Controller
Arduino

Phagestat
Lagoon Controller
Arduino

Phagestat
Lagoon Controller
Arduino

Phagestat
Lagoon Controller
Arduino
Bluetooth

RF Link

Raspberry Pi
Debian Linux
Remote Desktop
OpenCV
Python

Bluetooth Serial

Nutrient
pump + valve

Host Cell
pump + valve

Waste/Samplepump + valve

camera

magnetic mixer

aeration
Cellstat

Nutrient heater Host cell heater

PIR Temp Sensor

lights

Bluetooth
Communication

Bluetooth Serial

Arduino
Mini Pro

mixer
light
heater
 T sensor

valve
valve
valve
valve
Phagestat
1 of 4
Software Architecture

Raspberry Pi:
1. Level detection (levelapp.py, observe.py)
2. Turbidity measurement (turbid.py)
3. Bioluminescence detection (fluor.py)
4. Temperature controls (Nutrient, Inducers, Host culture)
5. Light control
6. Logging
7. Sampling? (currently stand-alone auto-sampler)

Arduino:
1. lagoon.ino (main controller routine)
  Controls magnetic mixer and meniscus light via commands from the system controller, regulates lagoon temperature using local temperature sensor
2. valves.h (multiple valve controller object)
  Autonomously opens valves on a regular schedule which is then adjusted via communication with the System controller, which has eyes on the liquid levels
3. pid.h (PID controller object)
  Proportional/Integral/Differential temperature/heater control